## Slide 1: AR communication protocol
Bart Tiemersma

## Slide 2: System overview
IMEC Eindhoven is responsible for everything left of the dashed line, IMEC Ghent for the part on the right
The memory mapped file is updated according to the communication protocol
Processing
Goggles
Game
Bluetooth
Memory mapped file

## Slide 3: Layout of memory mapped file
Index [bytes] | Name | Size [bytes] | Permissions of processing block | Permissions of game | Notes
0 | Version | 1 | Read only | Read only | Currently version “1”
1 | Up | 1 | Write only | Read/Write | Boolean, {0,1}
2 | Down | 1 | Write only | Read/Write | Boolean, {0,1}
3 | Left | 1 | Write only | Read/Write | Boolean, {0,1}
4 | Right | 1 | Write only | Read/Write | Boolean, {0,1}
5 | Blink | 1 | Write only | Read/Write | Boolean, {0,1}
6 | CalibrationStimulus | 1 | Write only | Read only | Currently unused
7 | ProgramState | 1 | Read only | Write only | Currently unused

## Slide 4: Protocol
Version 1
The protocol version is only set when the file is created by the server
The four types of saccades (up, down, left, right), as well as blinks, are reported like this:
  The server sets the corresponding Boolean to “True” when a new event is detected
  The client monitors these Booleans, processes the new events and resets them to “False” after handling the events
During calibration, the server communicates the stimulus to the client through the “CalibrationStimulus” field
  Currently unused, just a placeholder
The client reports its state to the server through the “ProgramState” field
  This will be used to inform the server about the start and end of the calibration

## Slide 5: Notes
A reference implementation for this communication protocol is included
  Tested on Python 3.6.2
  For testing this interface, ensure both client and server are either 32-bits or 64-bits applications and are in the same folder
  The processing block would be the server and the game would be the client
    The server is started first and is responsible for creating the file
  For a list of available commands, look at lines 82 and beyond in the file Server.py
Do not try to read or modify the file, only read and modify the memory map
The functionality of the fields “CalibrationStimulus” and “ProgramState” have yet to be defined